Bodger’s Guide #7

# A simple PSU, control and sequencer for a large GaAs PA

# Introduction

I was given the task of putting together the 10GHz transverter system for use during the Camb-Hams DXpedition to Mull in 2012. It uses a DB6NT transverter and a Mikom 10 Watt SSPA.  Now this PA is a “bit of an animal” requiring a drain supply of 11Volts at nearly 10 Amps to produce 10 Watts of RF at 10GHz. It also requires a negative 9 volt supply at a few mA and a TTL logic “low” to enable it.

I suspect that like all depletion mode GaAsFETs if the negative supply is removed from the Amplifier while the drain supply is switched on, the amplifier will rapidly become a very nice doorstop! In depletion mode FETS the channel is active even with zero volts on the gate, and a negative supply turns the device off.

So the main requirements were a Supply that runs from a 13.8V PSU, with failsafe protection against the removal of the negative supply.

To complete the control board requirements I needed a TX-RX sequencer that can fire a 12V latching coaxial antenna changeover relay and enable the PA. For this I incorporated a variant of my reliable “PICwencer” circuit and code (Ref 1)

While designed for a specific application, the circuitry and PIC code are easily adaptable for a number of PA and relay applications.

# Block Diagram

Figure 1 Controller Block Diagram

# Circuit description

Please refer to Figure 1 and Figure 2.

A transient suppression and protection Zener D5 protects the negative voltage regulator and electrolytics from an accidental supply above 16Volts.

The Negative Supply U$3 uses a MAX764 switch mode power supply IC, Resistors R14, 18 and 16 determine the output voltage.

The 12F629 8 pin DIL PIC IC3 uses its own internal clock and is powered from a 5V linear regulator U$4. The switching outputs GP0and GP1 of the PIC feed the TX and RX relays; the PIC generating a short pulse to trigger the relay via inverters Q1 and Q2 and source follower twin Power FETS U$2. The PTT input from the transverter is applied to GP3, resistive divider R1 and R2 allowing it to be fed direct from the 12 Volt level DB6NT transverter PTT out. GP4 feeds the TTL level signal direct to the PA,  Low = enabled, and the dual FET U$1 provides 12V buffered outputs from the PIC, but are not used in this application and need not be fitted.

The high current 11Volt linear regulator uses parallel LM1084 low-dropout 5 Amp regulators with balancing resistors R15 and R17 in the outputs to facilitate current sharing. Q3 in the “adj” legs ensures that the 11V supply is only enabled when the negative supply is present via D1. The PCB provides the facility to run a separate negative voltage sense wire right up to the PA connector, to protect against a broken -9.5 volt wire if you wish, or they can just be linked at the PCB.

# Circuit Diagram

Figure 2 Circuit Diagram

# PCB layout

I used surface mount technology allowing the PCB to fit inside a standard Schuberth tinplate box of dimensions 55.5 x 74 x 30mm. (see Reference 3) Layout is mainly surface mount apart from the PIC which is a standard 8-pin DIL package in a socket to allow easy program changes. The PIC is fitted on the opposite side of the board to the SMD components. The linear regulators are best mounted off the PCB and must be on a suitable heatsink such as that used by the PA itself.

If surface mount scares you, there is no reason why the circuit could not be adapted to use through-board components, and built on Veroboard or your own PCB, as all the devices should have leaded equivalents. The relay FETSs just need to be able to handle the current pulse drawn by the coax relay you use.

Figure 3 Component layout

The “Eagle” schematic and my PCB layouts are downloadable from my Website (see reference 2), The circuit and PCB layout are © Bravo Alpha Oscar 2012 not to be resold or used for any  commercial purposes whatsoever without written permission from the author .

# PCB Mask

The PCB mask below should be scaled to 72 x 55mm. The board is double sided FR4, and Copper is shown as white. There are a number of vias (shown as small green squares in Figure 3) that need to be linked to the bottom side ground plane.

Figure 4 PCB mask

# Parts list

| Part | Value | Package |
| --- | --- | --- |
| C1 C3 C4 C7 C14 C13 | 0.1uF | C0805 |
| C5 C6 C11 | 10uF | SANYO-OSCON_SMD_A5 |
| C10 | 150uF | SMC_D |
| C15 | 47uF | SANYO-OSCON_SMD_A5 |
| D1 D2 D3 D4 | BZX84CSMD | TO236 |
| D5 | TVS 16V | SMBG |
| IC2 | LM1084-V | 317TS |
| IC3 | PIC12F629P | DIL8 |
| IC4 | LM1084-V | 317TS |
| L2 | 47uH | POWER-CHOKE_WE-TPC |
| Q1 Q2 Q3 | BC847BSMD | SOT23 |
| R1 R2 | 10k | R0805 |
| R3 R4 | 1k2 | R0805 |
| R5 R7 | 10 | R0805 |
| R6 | 820 | R0805 |
| R8 | 100 | R0805 |
| R9 R10 R12 R13 R21 | 12k | R0805 |
| R11 | 1k5 | R0805 |
| R14 R18 | 750k | R0805 |
| R15 R17 | 0.01R | R2512 |
| R16 | 120k | R0805 |
| R19 | SOT | R0805 |
| R20 | 470 | R0805 |
| U$1 U$2 | FDC6401N | SOT23-6L |
| U$3 | MAX764CSA | SO08 |
| U$4 | LM317SO8 | SO-08 |

# Firmware

The PIC firmware source code can be downloaded from the “Downloads” page of my website. See reference 2.

Like the PCB layout is © Bravo Alpha Oscar 2012 not to be resold or used for any commercial purposes whatsoever without written permission from the author. Should you make improvements or modify it, in the spirit of sharing, please send me a copy of your updated code. `

In simple terms here is what it does

Power up, set relay to RX (pulse GP0 high)

; and ensure +5 to PA PTT line.(GP4 high) PA is disabled

;   wait for PTT to go low (GP3)

;   at PTT low, immediately set relays to TX (pulse GP1 low)

;   wait for relay to settle

;	put GP4 low to apply 0V to PA PTT line

;   wait for PTT to go high.

;   at PTT high, wait 25ms to allow drive to drop

;       apply +5V to PA PTT (GP4 low)

;       set antenna relay to RX again (pulse GP0 low)

;   wait for PTT to go low (GP3)

# References

- Worsnop J. C  The PICwencer” A processor - based relay sequencer for Amateur Radio antenna changeover control -  Scatterpoint October 2005

- www.g4bao.com

- Tinplate boxes via Alan Melia G3NYK alan.melia@btinternet.com

# Text boxes

From -9.5Vreg

To relay

To PA

To PA

To PA and11V reg

+13.8V

Relay FET Switches

11Volt 10 Amp Linear regulator

PIC controller

PA on off control FETS

-9.5V Switch mode regulator

5V Linear regulator