# A simple PIC controller for the G4JNT LMX2541 synthesiser board

John C Worsnop. PhD CEng MIET, G4BAO

## Introduction

G4JNT's LMX2541 synthesiser boards are described in (1). This board provides the hardware to run G4JNT's PIC code (2) and was made for the UK 432MHz beacon upgrades. It is based on G4JNT's original PIC controller described in (1) but does not have the on board GPS engine. It is designed to be used with an external G3RUH GPSDO (3) or similar unit that provides a serial NMEA stream and a 1pps clock pulse. It is also a useful, with suitable firmware, as a general purpose PIC controller for use with other serially programmed synthesisers.

No description of the PIC code is given, but see G4JNT's website (4) for some example code.

The PCB has a standard Microchip ICSP (in circuit serial programming interface) to allow programming of the chip, and is designed to fit in to a readily available 37 x 74 x 30mm tinplate box [5], if necessary.

## Circuit description

Figure 1 circuit diagram

An 18 pin DIL PIC16F628P Flash programmable PIC, IC1 is used to contain the main program. A regulated 5 V supply is provided by IC2 and associated components. The board has 3 interface ports

## ICSP port X1

X1 provides a standard Microchip ICSP (in circuit serial programming interface) to allow programming of the PIC.

## Synthesiser  control interface X2

A standard SPI 3-wire interface connects to the synthesiser board utilising RA0, RA1, and RA2 to provide Data, Clock and Load lines respectively.

## GPS interface X3

The 1PPS signal from the GPSDO is buffered by Q2 and fed to RB0 of the PIC. The NMEA signal from the TXD line of the GPS receiver is buffered by one half of the dual FET UIG2 and fed to RB1. Should A1A keying or other TX control be required by the beacon, an optional ON/OFF keying output is derived from RA5 and buffered by the other half of the dual FET U1G1. This is not implemented in the 432MHz beacons.

## Construction

Figure 2 PCB layout (component side)

The controller is built on standard FR4 PCB material with the 10MHz crystal, connectors and the PIC on the ground plane side. All the other components are surface mounted on the component side.

# Table 1 - Component list

| Component | Value | Type |
| --- | --- | --- |
| R1 | 15k | SMD 0805 |
| R3 | >180R (to suit LEDs) | SMD 0805 |
| R2, R4 | 1k | SMD 0805 |
| C1 | 330nF | 0805 |
| C2 | 10uF 16V | SMD electrolytic |
| C4,C5 | 22pF | ceramic 0805 |
| C3, C6 | 100nF | ceramic 0805 |
| IC1 | 16F628P | 18 pin DIL PIC |
| IC2 | 78L05 | SMD 5V 100mA regulator |
| U$1 | FDC6401N | Dual N channel MOSFET |
| Q1 | 10MHz Crystal |  |
| Q2 | BC847 or similar | NPN transistor SMD |
| LED 1 | Red LED | SMD 0805 |
| LED 2 | Green LED | SMD 0805 |
| D1 | Schottky diode | SMD |
| X1 to 3 | 6 pin Berg pin headers |  |

# References

- The G4JNT LMX2541 Fractional-N synthesiser development PCB http://g4jnt.com/LMX2541_Synth_Module.pdf

- Some example PIC code from G4JNT http://g4jnt.com/LMX2541_WSJT_Routines.zip

- The G3RUH GPSDO http://www.jrmiller.demon.co.uk/projects/ministd/frqstd.htm

- G4JNT's Website http://g4jnt.com

- Tinplate boxes can be obtained from Alan Melia G3NYK at http://g3nyk.ham-radio-op.net/componen.htm