The Bodger’s Guide to …………..

A high-side/low side 432MHz Receiver downconverter for use with the SDR-IQ and similar 28MHz receivers

# Introduction

I have “got used” to using my SDR-IQ receiver on the microwave bands, and I have a switching box with a 144MHz – 28MHz downconverter that enables me to use it as a separate receiver on all bands.

This articles describes a 432MHz receive downconverter that uses the SDR kits QRP2000 USB-synthesiser (Reference 1) as an external local oscillator. This allows it to operate with the LO either 28MHz above or below the 432MHz band.

Note that you need to order the version of the QRP2000 with the Si570BBB000141DG device covering up to 810 MHz. See Reference 1 for details

# So why no Bodger’s LO design then?

Two things drove this converter and its slightly unusual approach.

- I recently set up to operate on 70cm, and quite frankly, missed the SDR facility!

- My latest 24GHz system uses a Thales Module with a 432MHz  IF, but with high side LO injection, meaning that with a conventional 432MHz converter, the SDR-IQ would have to tune backwards,  28-26MHz and be switched to LSB.

- I could see no reason to “reinvent the wheel” when such a good LO was available as a kit

Using a synthesised LO means that I can operate it at 404MHz directly from the 70cms antenna or at 460MHz to down convert the 24GHz 432MHz high side IF and tune 28-30MHz USB as normal.

You may wish to simply use this downconverter design with your own LO and switchable crystals or synthesiser, but I have used the USB-synth as an LO source multiplied up 192 times as a 24 GHz source and it is really excellent.

# Circuit description

The circuit design is very straightforward.

IC1  is a voltage regulator allowing the circuit to operate from a raw supply up to 27 volts.

IC2 is a MGA-62560 pHEMT gain block matched to the 70cms band with C2 and L2.

The IF filter U$2 is a TA0693A 10MHz wide SAW filter, centred on 435MHz.

The diode mixer M1 is a 500MHz, +7dBm LO mixer from Mini-Circuits. The IF output is terminated with a diplexer designed to pass 28MHz and remove other signals from the mixer output.

# Circuit Diagram

# PCB layout

The PCB is made from 1.6mm FR4 material, is designed to fit in a standard tinplate box and can be terminated on the box with the connectors of your choice.

71mm

Eagle files  for the PCB can be downloaded from www.g4bao.com

# Component list

| Component | Value | Type |
| --- | --- | --- |
| C1 | 0.33uF | SMD X7R ceramic |
| C2, C7 | 100pF | SMD 0805 NPO ceramic |
| C3 | 10uF | SMD aluminium electrolytic |
| C4 | 100nF | SMD 0805 NPO ceramic |
| C5 | 68pF | SMD 0805 NPO ceramic |
| C6 | 10pF | SMD 0805 NPO ceramic |
| C8 | 4p7 | SMD 0805 NPO ceramic |
| C9, C10, C11 | 150pF | SMD 0805 NPO ceramic |
| R1 | 390 ohms | SMD 0805 |
| R2 | 270ohms | SMD 0805 |
| L1 | 1uH | SMD 0805 |
| L2 | 4.7nH | SMD 0805 |
| L3 | 47nH | SMD 0805 |
| L4 | 200nH | SMD 0805 |
| L5 | 200nH | 0805 |
| IC1 | LM317M | 8 pin SMD package Farnell 1652326 |
| IC2 | MGA-62563 | Farnell 7820453 |
| F1 | TA6093A | Golledge 435MHz, 10MHz wide SAW filter http://www.golledge.com/pdf/products/saw/gsrf.pdf |
| M1 | RMS-1 or similar 500MHz level 7 mixer | Mini circuits. http://www.minicircuits.com/pdfs/RMS-1.pdf look on EBay for similar devices |

# Representative test results

These figures show the results measured with a high side LO at 460MHz.

N.B they are measured on Amateur test equipment which does not have a current calibration certificate. They should be treated as a guideline only, and no performance guarantees are given or implied.

# References

- USB Synth kits http://sdr-kits.net/QRP2000_Description.html

- Eagle files can be downloaded at www.g4bao.com

- Free “Eagle” PCB Software from CADsoft  http://www.cadsoft.de/

# Copyright notice

This design is © 2011 to John Worsnop trading as Bravo Alpha Oscar.  It may be used, copied and modified by Amateur radio experimenters only. No commercial exploitation or use is allowed without the express permission of the copyright owner.